## Slide 1: Raman Spectroscopy Data Exploration & Modeling Strategy for Cysteine Prediction in Pea Cultivars
Date: June 10, 2026
Presented by Priyanshu Mittal

## Slide 2: Dataset Overview
20 pea cultivars, 324 spectra each = 6480 total
Each Spectrum: 1530 data points
Raman Shift range: 97.8 – 3361.7 cm^-1
Labels: Cysteine concentration (g/100g) per cultivator
Data collected across 3 field locations: Limerick, Rosthern, Sutherland
One file per spectrum, semicolon-delimited text format
Usable data starts at pixel 518

## Slide 3: Dataset Anomalies
CDC Jasper – No spectral files found, only system metadata.
  Status - Solved
CDC Inca – Initially had 432 spectra instead of 324.
  Status - Solved
Redbat 88 – 323 spectra
  Status – Need to go through

## Slide 4: Cysteine Concentration Distribution
Notes:   Range: 0.312 – 0.373 g/100g (spread of only 0.061)
  Mean: 0.34 g/100g
  Highest: CDC Spectrum (0.3732)
  Lowest: CDC Meadow (0.3120)
  Narrow range makes this a challenging regression problem

## Slide 5: Individual Cultivar Spectra
Notes:   All cultivars share the same overall spectral shape
  Dominant peak at ~200 cm⁻¹, smaller peaks at ~750 and ~1000 cm⁻¹
  Within-cultivar spread varies, some cultivars (e.g. CDC Greenwater) show much higher replicate variability than others
  Y-axis scales differ between cultivars → intensity normalization will be critical

## Slide 6: All Spectra Combined
Notes:   Top panel: large intensity scaling differences across all spectra
  Bottom panel: mean spectra overlap heavily, no clear visual separation between high and low cysteine cultivars
  Subtle differences exist but are not visible → machine learning needed

## Slide 7: Variability Analysis
Notes:   Within-cultivar variability is highest at the main peak (~200 cm⁻¹)
  Between-cultivar variability also peaks at ~200 cm⁻¹, most of the difference between cultivars is intensity scaling, not unique spectral features
  Both sources of variability drop sharply after 500 cm⁻¹
  Confirms that preprocessing (especially SNV normalization) is essential before modeling

## Slide 8: Proposed Preprocessing
Raw Spectrum
Savitzky-Golay Smoothing
(To remove noise)
Baseline Correction (remove fluorescence)
Why each step:
SG Smoothing: reduces noise without distorting peaks
Baseline Correction: removes broad fluorescence background
SNV: fixes the large intensity differences seen in plots
Derivative: enhances subtle differences between cultivars
SNV Normalisation
(fix intensity scaling)
1st and 2nd Derivative (enhance subtle oeak differences)

## Slide 9: Proposed Models
Partial Least Square Regression (PLSR) | Standard for spectroscopy, works well with small datasets
Support Vector Regression (SVR) | Robust to overfitting, handles high emissions
Principal Component Regression (PCR) | Simple baseline comparison to PLSR
Random Forrest | Captures non-linear relationships
1D-CNN | Learns spectral patterns automatically

## Slide 10: Evaluation Strategy
Why not random split?
  Spectra from the same cultivars share one label.
  Random splitting would leak information and inflate performance.
Approach: Leave One Cultivar Out Cross Validation
  Hold out all 324 spectra from one cultivar
  Train on remaining 19 cultivars
  Predict held-out cultivar
  Repeat 20 times

## Slide 11: Summary
Dataset fully explored: 20 cultivars, 6,480 spectra
Key challenge: narrow cysteine range (0.061 g/100g spread)
Preprocessing pipeline defined
Modeling strategy ready