## Slide 1: Cysteine Prediction in Pea Cultivars using Raman Spectroscopy and Machine Learning
July 16, 2026

## Slide 2: LSTM – Long Short-Term Memory
LSTM stands for Long Short-Term Memory, a type of recurrent neural network (RNN) designed to handle sequences where context from much earlier in the input still matters.
The core idea behind LSTMs is a gating mechanism that regulates information flow through the network.

## Slide 3: KEY CONCEPT
Unlike CNN which looks at local windows, LSTM maintains a memory that carries information across the entire 1,530-point sequence. It decides what to remember, what to forget, and what to output at each step using three gates:
Bidirectional LSTM: Our LSTM reads the spectrum in both directions simultaneously: left to right AND right to left. This means a peak at 200 cm⁻¹ can influence the prediction based on what happens at 1,500 cm⁻¹ and vice versa.
Input gate → decides what new information to store
Forget gate → decides what old information to discard
Output gate → decides what to pass to the next step
Forward LSTM: 97.8 cm⁻¹ → 200 cm⁻¹ → ... → 3361.7 cm⁻¹
Backward LSTM: 3361.7 cm⁻¹ → ... → 200 cm⁻¹ → 97.8 cm⁻¹
Combined output at each step

## Slide 4: LSTM - Architecture:
Total parameters: 545,921 : lightest of all three DL models

## Slide 5: LSTM Code Step by Step
Step – 1: Reshape Input:
Step - 2: Bidirectional LSTM processes sequence:
Step – 3: Fully Connected prediction:
Raw spectrum: (batch, 1530)
Reshaped to: (batch, 1530, 1)
↑ each wavenumber = one time step with 1 feature
Forward pass: reads from wavenumber 97.8 to 3361.7
Backward pass: reads from wavenumber 3361.7 to 97.8
At each step: outputs 128 + 128 = 256 features
Final output: last time step → (batch, 256)
256 features → 64 → 1 (cysteine value)
Dropout 0.3 applied between layers

## Slide 6: LSTM Code Step by Step
Step – 4: Key difference from CNN:
Step – 5: Why LSTM is slower than CNN:
CNN: sliding window sees 5 consecutive points at a time
LSTM: sees ALL 1530 points sequentially, remembers context
CNN: convolves all positions simultaneously (parallel)
LSTM: must process each of 1530 time steps sequentially (Cannot be fully parallelised — slower on GPU)

## Slide 7: LSTM Preprocessing Comparison
SG + MSC performs best for both 80/20 and LOCO. MSC corrects multiplicative scattering effects, which benefits sequential processing.
80/20 is very low across all combinations. LSTM struggles with within cultivar discrimination.
Preprocessing | RMSE 80/20 | R² 80/20 | RMSE LOCO | R² LOCO | RPD LOCO
SG + SNV | 0.0162 | 0.0202 | 0.0114 | 0.5236 | 1.4488
SG + MSC | 0.0143 | 0.2348 | 0.0091 | 0.6918 | 1.8014
SG + 1st Deriv | 0.0163 | 0.0113 | 0.0109 | 0.5605 | 1.5085
SG + 2nd Deriv | 0.0163 | 0.0061 | 0.0115 | 0.5143 | 1.4349
SG + SNV + 1st Der | 0.0164 | 0.0004 | 0.0112 | 0.5364 | 1.4687
SG + SNV + 2nd Der | 0.0164 | 0.0007 | 0.0112 | 0.5366 | 1.4690
SG + MSC + 1st Der | 0.0161 | 0.0372 | 0.0109 | 0.5605 | 1.5085
SG + MSC + 2nd Der | 0.0162 | 0.0225 | 0.0115 | 0.5143 | 1.4349
Raw | 0.0161 | 0.0335 | 0.0093 | 0.6772 | 1.7602

## Slide 8: LSTM Final Results
LOCO : Good generalization to unseen cultivars.
80/20 : Weak within cultivar discrimination compared with CNN and CNN LSTM.
Metric | 80/20 Split | LOCOCV
RMSE | 0.0143 | 0.0091
R² | 0.2348 | 0.6918
RPD | 1.1432 | 1.8014
Preprocessing | SG + MSC | SG + MSC

## Slide 9: CNN-LSTM
The CNN LSTM architecture involves using Convolutional Neural Network (CNN) layers for feature extraction on input data combined with LSTMs to support sequence prediction.
A CNN LSTM can be defined by adding CNN layers on the front end followed by LSTM layers with a Dense layer on the output.

## Slide 10: Key Concept – CNN LSTM
CNN extracts local peak features from the spectrum.
Compresses 1,530 spectral points into 191 feature vectors.
LSTM processes these feature vectors as a sequence.
Captures long range relationships between spectral regions.
Combines local feature extraction with sequential learning for improved performance.

## Slide 11: CNN-LSTM ARCHITECTURE
Notes: Why combine CNN and LSTM:
CNN alone: great at local features, misses long range spectral relationships
LSTM alone: captures long range context but struggles with raw 1,530 point sequences
CNN-LSTM: CNN reduces sequence length from 1,530 to 191 making LSTM more efficient, while LSTM captures relationships between distant spectral regions

## Slide 12: CNN-LSTM Code Step by Step
Step 1: CNN extracts features
Step 2: Reshape for LSTM
Input: (batch, 1530)
↓ unsqueeze
(batch, 1, 1530)
↓ 3 Conv blocks with MaxPool
(batch, 64, 191)
1530 / 2 / 2 / 2 = 191 time steps
each with 64 learned features
CNN output: (batch, 64, 191)
↓ permute dimensions
LSTM input: (batch, 191, 64)
191 time steps, 64 features each

## Slide 13: CNN-LSTM Code Step by Step
Step 3 : LSTM reads feature sequence
Step 4 : Final prediction
Bidirectional LSTM processes 191 steps
Forward: step 1 → step 2 → ... → step 191
Backward: step 191 → ... → step 1
Last step output: (batch, 256)
256 → 64 → 1 (cysteine value)

## Slide 14: Key advantage over standalone LSTM:
Model | Processing | Efficiency
LSTM | Processes all 1,530 raw spectral points sequentially | Slow due to long sequence length
CNN LSTM | CNN compresses the input to 191 feature vectors before LSTM processing | 8× fewer LSTM steps, faster and more meaningful input

## Slide 15: CNN-LSTM Preprocessing Comparison
SG + SNV performs best for LOCO (), unlike standalone CNN where raw spectra performed best.
80/20 , indicating limited within cultivar discrimination, similar to the standalone LSTM.
Preprocessing | RMSE 80/20 | R² 80/20 | RMSE LOCO | R² LOCO | RPD LOCO
SG + SNV | 0.0142 | 0.2496 | 0.0086 | 0.7282 | 1.9183
SG + MSC | 0.0141 | 0.2547 | 0.0091 | 0.6937 | 1.8068
SG + 1st Deriv | 0.0160 | 0.0466 | 0.0107 | 0.5729 | 1.5302
SG + 2nd Deriv | 0.0162 | 0.0166 | 0.0106 | 0.5818 | 1.5463
SG + SNV + 1st Der | 0.0153 | 0.1242 | 0.0108 | 0.5718 | 1.5281
SG + SNV + 2nd Der | 0.0154 | 0.1147 | 0.0105 | 0.5934 | 1.5683
SG + MSC + 1st Der | 0.0154 | 0.1205 | 0.0108 | 0.5700 | 1.5250
SG + MSC + 2nd Der | 0.0154 | 0.1178 | 0.0106 | 0.5848 | 1.5519
Raw | 0.0162 | 0.0224 | 0.0091 | 0.6959 | 1.8133

## Slide 16: CNN-LSTM Final Results
Best LOCO RMSE = 0.0086, the lowest prediction error among all three deep learning models.
LOCO RPD = 1.918, close to the acceptable value of 2.0, but standalone CNN performs better (RPD = 2.148).
Metric | 80/20 Split | LOCOCV
RMSE | 0.0142 | 0.0086
R² | 0.2496 | 0.7282
RPD | 1.1544 | 1.9183
Preprocessing | SG + SNV | SG + SNV

## Slide 17: Deep Learning Model Comparison
CNN with raw data performs best overall, with the highest LOCO (0.7833) and RPD (2.148).
CNN LSTM gives the lowest LOCO RMSE (0.0086), showing the most accurate predictions.
All three deep learning models achieve positive LOCO , demonstrating good cross cultivar generalization.
Models with an LSTM component have low 80/20 , indicating limited within cultivar discrimination.
Model | Best Config | 80/20 R² | LOCO R² | LOCO RPD
CNN | SG + SNV | 0.7828 | 0.6863 | 1.786
CNN | Raw | 0.7027 | 0.7833 | 2.148
CNN-LSTM | SG + SNV | 0.2496 | 0.7282 | 1.918
CNN-LSTM | Raw | 0.0224 | 0.6959 | 1.813
LSTM | SG + MSC | 0.2348 | 0.6918 | 1.801
LSTM | Raw | 0.0335 | 0.6772 | 1.760